## Slide 1: Lecture # 04
Prepared by: tahmina khan

## Slide 2: 8086 Addressing modes
The CPU can access data in various ways called addressing modes.
There are seven types of addressing modes which are:
Register
Immediate
Direct
Register indirect
Based relative
Indexed relative
Based indexed relative

## Slide 3: Register Addressing Mode:
It means that the register is the source of an operand for an instruction.
Examples for using this mode are:
MOV CX,AX
MOV DS,CX
MOV BX,DX
MOV SI,CX
MOV AH,BL
MOV DL,CH

## Slide 4: Immediate Addressing Mode:
In this mode, the source operand is a constant.
This mode can be used to load information into any of the registers except the segment register and flag register.
Examples for using this mode are:
MOV AX,2550H
MOV SI,6254H
MOV BP,A34CH
MOV CL,64H
To move information to the segment registers, the data must first be moved to a general purpose register and then to the segment register. Example:
MOV AX,9865H
MOV DS,AX
MOV DS,9865H is illegal

## Slide 5: Direct Addressing Mode:
In this mode, the data is in some memory location and the address of the data in memory comes immediately after the instruction.
Note that in immediate addressing, the operand itself is provided with the instruction, whereas in direct addressing, the address of the operand is provided with the instruction. This address is the offset address.
Some examples are:
MOV DL,[2400]
MOV [3457],AL
MOV AH,[ADEF]

## Slide 6: Example:
Find the physical address of the memory location and its contents after the execution of following commands, assuming that DS = 1512H
MOV AL, 99H
MOV [3518], AL
Solution:
By using segment register and offset register, we have to find physical address.
DS : offset
1512 : 3518
Physical address = (DS x 10H) + offset
Physical address = 18638H
It means that after the execution of commands, the memory location with address 18638H will contain the value 99H.

## Slide 7: Register Indirect Addressing Mode:
It allows data to be addressed at any memory location through an offset address held in any of the following offset register: BX, BP, SI and DI.
Some examples to execute this addressing mode are:
MOV AL, [BX]
MOV CL, [SI]
MOV [DI], AH

## Slide 8: Example:
Assume that DS = 1120H, SI = 2498H and AX = 17FEH. Show the contents of memory location after the execution of “MOV [SI], AX”
Solution:
The contents of AX are moved into memory locations with logical address DS:SI and DS:SI+1.
Physical address = (DS x 10H) + SI
= 11200 + 2498
= 13698H
It means that after the execution of command, the memory location 13698H will contain the value FE, the low byte and 13699H will contain the value 17, the high byte.

## Slide 9: Based Relative Addressing Mode:
This mode only contains the base registers (BX or BP) with some displacement, which is used to calculate the effective address.
Some examples to execute this mode are:
MOV CX, [BX]+10
MOV AL, [BP]+5
MOV [BX]+50, DL
The above command can also be written as:
MOV [BX+50], DL
Physical address for this mode can be calculated as:
Physical Address = (DS x 10H) + BX + displacement
or
Physical Address = (SS x 10H) + BP + displacement

## Slide 10: Indexed Relative Addressing Mode:
This mode only contains the index registers (SI or DI) with some displacement, which is used to calculate the effective address.
Some examples to execute this mode are:
MOV CX, [SI]+100
MOV AL, [DI]+25
MOV [SI]+500, DL
The above command can also be written as:
MOV [SI+500], DL
Physical address for this mode can be calculated as:
Physical Address = (DS x 10H) + [SI] + displacement
or
Physical Address = (DS x 10H) + [DI] + displacement

## Slide 11: Based Indexed Relative Addressing Mode:
This mode contains the base registers (BX or BP) as well as index registers (SI or DI) with some displacement, which is used to calculate the effective address.
Some examples to execute this mode are:
MOV CX, [BX][SI]+30
MOV [BX][DI]+250, DL
The above command can also be written as:
MOV [BX+DI+250], DL
Physical address for this mode can be calculated as:
Physical Address = (DS x 10H) + BX + SI + displacement
or
Physical Address = (DS x 10H) + BX + DI + displacement

## Slide 12: Example:
Assume that DS = 4500H, SS = 2000H, BX = 2100H, SI = 1486H, DI = 8500H, BP = 7814 and AX = 2512H. Show the exact physical memory location where AX is stores in each of the following.
MOV [BX]+20, AX
MOV [SI]+10, AX
MOV [DI]+4, AX
MOV [BP]+12, AX
Solution:
In each case PA = (segment register x 10H) + offset register + displacement.
DS:BX+20 location 47120 = 12 and 47121 = 25
DS:SI+10 location 46496 = 12 and 46497 = 25
DS:DI+4 location 4D504 = 12 and 4D505 = 25
SS:BP+12 location 27826 = 12 and 27827 = 25